## Slide 1
Dec 3, 2024
D. Ratner
SLAC National Accelerator Laboratory
Taste of Machine Learning Applications at SLAC

## Slide 2
Outline
Surrogate models
Optimization
Anomaly detection
Reconstruction/Inverse problems
LLMs

## Slide 3
Outline
Surrogate models
Optimization
Anomaly detection
Reconstruction/Inverse problems
LLMs

## Slide 4: Surrogate Models: Motivation
A. Edelen et al, ml4physics, NeurIPS, 2020
A. Edelen
Motivation:
Reduce computational cost: AI models can many orders of magnitude faster!
  Note that training is expensive!  requires running physics simulator and than training of surrogate
  Need frequent use of surrogate to justify
  (“amortization”)
Surrogate models: AI approximations of physics simulations
Can be updated directly on experimental data (“Digital twins”)
  Train on simulations + experiments
   More accurate than physics sim!
Provide automatic derivatives
Notes: Genesis simulations provide users very accurate prediction of X-ray pulses for preparing for shifts and testing analysis methods. However, each simulation takes ~1000s of CPU-seconds. For users who require large numbers of examples, e.g.crystallography or statistical methods like ghost imaging, Genesis is too slow.
Generative adversarial networks (GANs) use two networks: the “discriminator” tries to identify if an example is real (i.e. Genesis), or fake (i.e. the “generator”). The generator tries to fool the discriminator. As the two networks fight, the generator makes more and more realistic examples. Images at right show a generated fake XTCAV image (upper right) and the associated X-ray profile (lower right, green). The blue curve is what the old XTCAV algorithm would have estimated from the fake example, showing that the generated example is reasonable.

## Slide 5: Surrogate Models: Applications
Designing new machines: surrogate executes faster than physics sim
LCLS-II simulations, Y. Ding, J. Qiang
Live tuning of machines: surrogate trained during optimization
AI-based analysis: e.g. physics-informed NN to reconstruct physical observables/parameters
ρ = 0.7
ρ = 0
J. Duris, PRL, 2020
“One-to-one” physics simulations take ~100k CPU hours
 Surrogate model <10-7 GPU hours
Applications for accelerators:

## Slide 6: Surrogate Models: Gaussian processes
AI Method: Gaussian processes
J. Duris, PRL, 2020
Instance-based learning (e.g. support vector machines, k-nearest neighbor)
Effective with a small number of samples
Provides estimate and uncertainties

## Slide 7
Outline
Surrogate models
Optimization
Anomaly detection
Reconstruction/Inverse problems
Large language models

## Slide 8: Optimization: Facility operation use case
Quadrupole magnets
Challenge: How to optimize a scientific facility? Many tuning knobs, acquisition is expensive ($50k/hour, ~$25M/year!), many operators/physicists to train
SoTA Problems: Manual tuning  slow, depends on operator experience
Numerical optimizers  ignores domain knowledge, inefficient
AI solution:
Model-based optimization leverages physics knowledge and past experience for efficient global optimization
Methods: Bayesian optimization (BO), reinforcement learning (RL)
Status:
BO in regular use for accelerators worldwide (10-100x speedup)
Active research in RL, NN priors, algorithmic execution (BAX), …

## Slide 9: Optimization: Facility design use case
Challenge: How to design a new facility? High-dimensional search (e.g. dozens of sextupoles for modern rings), expensive simulations (e.g. tracking ~106 turns)
SoTA Problems: Genetic algorithms are sample inefficient  limited to low-dimensions, short tracking
AI solution:
Neural network surrogates approximate expensive simulations
Optimal design methods to maximize efficiency (e.g. Bayesian algorithmic execution)
Status:
Factor of ~100x speed-up from NN-based search
Employed for ALS-U, SSRL-X, FCC, and other designs
Image courtesy J. Wan, Y. Jiao

## Slide 10: Optimization: Compound discovery
Challenge: How to discover a novel material? Design space is enormous (trillions of synthesizable drugs), and each measurement/calculation is costly.
SoTA Problems: Expert-guided search (e.g. hand-design of drugs by chemists). Efficiency directly corresponds to quality of final compounds.
AI solution:
Neural network surrogates predict properties
Optimal design methods to maximize efficiency (e.g. Bayesian algorithmic execution)
Status:
AlphaFold is now a core part of drug design
Experimental design for compound discovery still in early stages
S. Gasiorowski, D. Mendez, A. Cohen
S. Gasiorowski, M. Han, Y. Lin

## Slide 11: Optimization: Bayesian optimization
Acquisition point
Acquisition
function
Ground truth
Posterior
Model-based optimization
Gradient optimizer
Advantage 1: Balance “exploitation vs. exploration”
 Find global maximum
Bayesian optimizer
Mitch McIntire

## Slide 12: Optimization: Bayesian optimization
Measured
Modeled
Quad 1
Quad 1
Quad 2
Advantage 2: Existence of model enables use of physics, archived data
Model-based optimization
ρ = 0.7
ρ = 0
Groundtruth
Model,
no correlation
Model,
w/ correlation
e.g. learning correlations in data improves modeling
Bayesian Optimization of an FEL, Duris et al., PRL, 2020

## Slide 13
Outline
Surrogate models
Optimization
Anomaly detection
Reconstruction/Inverse problems
Large language models

## Slide 14: Anomaly detection: Facility prognostics use case
SLAC Linear Accelerator and 280 Overpass
SLAC RF Stations
Challenge:
Modern facilities have thousands of sub-systems
 frequent failures
 downtime, poor performance
SoTA Problems:
Millions of diagnostics  manual search infeasible
Simple thresholds are common  poor precision and/or recall
Recall = TP/(TP+FN) Precision = TP/(TP+FP)
TP = true positive, FP = false positive, FN = false negative

## Slide 15: Anomaly detection: Facility prognostics use case
SLAC Linear Accelerator and 280 Overpass
SLAC RF Stations
Challenge:
Modern facilities have thousands of sub-systems
 frequent failures
 downtime, poor performance
AI solution:
Neural networks learn normal distribution and identify outliers as anomalous
Unsupervised training  can train on years of 1Hz archived data
Inference is cheap  can run continuously

## Slide 16: Anomaly detection: Facility prognostics use case
SLAC Linear Accelerator and 280 Overpass
SLAC RF Stations
Example: RF station faults
RF stations provide power for acceleration
Most common fault at LCLS (1000s/year)
Degrades performance even if no downtime
Years of data, only dozens labeled
AI solution:
Neural networks trained to identify coincidence between beam and sub-system
50% better recall, 6x fewer false positives vs. SoTA (70% false positive  15% false positive)

## Slide 17: Anomaly detection: Physics discovery (ELMs)
Challenge: Identify edge-localized modes (ELMs) in tokomaks
Fusion-cdt
Green lines: existing State-of-art
Yellow bands: DNN trained with coincidence
F. O’Shea
ELMs result in beam loss and potential catastrophic damage
Terabytes of data, but mostly unlabeled
SoTA classical methods known to have recall <50%
Interferometers,
beam emission spectroscopy
Filterscopes

## Slide 18: Anomaly detection: Autoencoders
Accelerator diagnostics
Input
Latent space
Output
Accelerator diagnostics
Time (~1 minute)
Diagnostics
Reconstruction error
|Output – Input|
Ryan Humble
NN Autoencoder solution
Training step: train on auto-encoder on “normal data” (ideally without any anomalies)
Inference can use two methods
  Reconstruction error indicates sample from a new (i.e. anomalous) distribution
  Normal examples map to central portion of latent space. Distance in latent space then indicates anomalous behavior

## Slide 19
Outline
Surrogate models
Optimization
Anomaly detection
Reconstruction/Inverse problems
Large language models

## Slide 20: Inverse problems: AI methods
Challenge: How to solve a repeated inverse problem?
F
?
1. Solve optimization problem:
2. Train a neural network:
x
y
3. Train a cycle-consistent neural network:
X
Inputs
Y
Target
x
y
F
Caveat: F must be differentiable!

## Slide 21: Inverse problems: Pulse reconstruction use case
Input power points
(3fs FWHM resolution)
Input spectral power points (80meV FWHM resolution)
Maxwell, Timothy J., et al. International Society for Optics and Photonics, 2014.
power
Spectrum
Challenge: Given measured amplitude of power/spectrum at an x-ray free electron laser (XFEL), how to recover high-resolution field?
SoTA Problems:
Iterative inverse solver: guess solution and check
Too slow for a MHz XFEL, large phase errors
AI solution
NN solver is million fold faster at inference time
First consistent phase recovery

## Slide 22: Inverse problems: differentiable simulations
Key requirement for PINNs/cycle-consistent NN: differentiable simulator
LArTPC (e.g. DUNE) simulator:
S. Gasiorowski, Y. Nashed, Y. Chen, K. Terao et al.
MAGIS-100 simulator
Cheong, Sanha, et al (2022)

## Slide 23: Inverse problems: Single-particle imaging
Greg Pintilie
Kappel et al.
Single-particle imaging of biomolecules with Cryo-EM:
Structures for un-crystallizable proteins/RNA
Closer to in-vivo than a crystal
Access to conformations not just average structures

## Slide 24: Inverse problems: Single-particle imaging
Recast as a repeated inverse problem:
Density map
A million images  a million inverse problems
Each image requires pose and conformation estimation
F
Pose

## Slide 25: Inverse problems: Single-particle imaging
Encoder network
NMA
Decoder
Conformation Space
Orientation Space
Microscope Digital Twin
Input
Output
Forward model
Latent NMA representation
Learn network/model parameters by minimizing the difference between input and output images
Recent work: directly learn atomic model conformations on data
Parametrize atomic model with normal mode analysis (NMA)
Train encoder network to map each image to a point in NMA space
Differentiable simulation maps NMA space to atomic model to microscope image
Y. Nashed, F. Poitevin, et al., submitted (2024)
spliceosome

## Slide 26: Inverse problems: Single-particle imaging
First experimental results on spliceosome:
Absolute error
Signal-to-noise
A
NMA latent space
Observed motion
Fitting 16 normal modes, 140k particles, 128x128 images
Uncertainties from cross-validation (2 partitions)
Y. Nashed, F. Poitevin, et al.

## Slide 27
Outline
Surrogate models
Optimization
Anomaly detection
Reconstruction/Inverse problems
Large language models

## Slide 28
Large language models: Logbooks
Challenge: How to capture value of scientific documents (papers, logbooks, notebooks, wikis, etc)?
AI solution:
Large language models (LLMs) are adept at natural language queries
Complex queries of logbooks
Generation of novel text (e.g. shift summaries)
Meta-data generation
Status:
Early demonstrations, state-of-art is changing fast
More development needed for multimodal data, domain-specific data sources, etc.
“What is typical uncertainty of emittance measurements?"

## Slide 29
Large language models: Retrieval augmented generation
AI methods: Scientific language is highly specialized and may not be represented in generic LLMs. Two options:
Fine-tuning: Retrain using domain science texts. But expensive: requires data prep and compute
Retrieval Augmented Generation (RAG): Select “small” portion of relevant texts to use as context.
Courtesy Prompt Engineering Guide
Train an embedding on domain science texts
Learn embedding of all domain documents
For each query, select most relevant text (nearby in embedding space)
Feed relevant text as context along with prompt to generic LLM.

## Slide 30
Thanks for your attention!
Alex Bien, William Colocho, James Cryan, Joe Duris, Eric Darve, Auralee Edelen, Ryan Humble, TJ Lane, Siqi Li, Dylan Kennedy, Jason Liang, Alberto Lutman, Matt Gibbs, Xiaobiao Huang, Sara Miskovich, Willie Neiswanger, Finn O’Shea, Ryan Roussel, Zhe Zhang
Thanks to collaborators:
Caveat: This is just a taste of applications, far from a comprehensive review!

## Slide 31
Backup
Notes: Histogram of the events based on the change in RF amplitude. Orange were labeled anomalous by our algorithm. A simple threshold at ~5 would have significant differences (about 20%) from our NN prediction. Based on visual inspection and correlation efficiency, we believe the NN is mostly correct (~10% errors).

## Slide 32: Anomaly detection: Edge-localized modes
Challenge: Identify edge-localized modes (ELMs) in tokomaks
Fusion-cdt
Green lines: existing State-of-art
Yellow bands: DNN trained with coincidence
F. O’Shea
ELMs result in beam loss and potential catastrophic damage
Terabytes of data, but mostly unlabeled
SoTA classical methods known to have recall <50%
Interferometers,
beam emission spectroscopy
Filterscopes

## Slide 33: X-ray Pulse Reconstruction
Inverse problem: Full beam reconstruction
Advantages: 108 faster, higher accuracy on amplitude and phase compared to iterative method
D. Ratner et al., Opt. Exp., 2021

## Slide 34: Anomaly Detection: RF Station Faults
Existing solution #1: Thresholding on subsystem amplitudes
Readbacks of station power condensed to “status bit” for each of 80 stations
Status bit ‘0’ if healthy, and flips to ‘1’ if RF amplitude changes more than 2%
Status bit has multiple problems:
Too simplistic (only looks for sudden drops)
Too permissive (misses subtle faults)
Too noisy (lots of false positives)
7 example measurements
Time (min)
0
5
RF station amplitude for 1 station
70% of alarms are false
(i.e. poor precision)
RF station diagram
Recall = TP/(TP+FN) Precision = TP/(TP+FP)
TP = true positive, FP = false positive, FN = false negative

## Slide 35: Anomaly Detection: RF Station Faults
Operators watch for a drop in X-ray power here
After observing a drop, search for RF stations with warning/fail status
Existing solution #2: Manual, beam-based anomaly detection
Many missed events
(recall ~ 1%)

## Slide 36: Anomaly Detection: RF Station Faults
New approach: Beam-based algorithm inspired by operators
Highway 280
Algorithm #1 looks for subsystem anomalies
RF stations
Beam position monitors
Algorithm #2 looks at final beam quality
Simultaneous anomalies trigger alarm
Question: How do we train these algorithms with no labels?
Key insight: A ‘good’ pair of algorithms will be self-consistent

## Slide 37: Coincident Anomaly Detection (CoAD)
Consider two algorithms making predictions on two streams of data
Subsystem
Beam quality
Algorithm 1
Algorithm 2
Prediction
Unknown
machine state
Red stars = consistent
black stars = inconsistent
More red = higher recall;
less black = higher precision
Subsystem (s)
Quality (q)
Anomaly
confidence
Anomaly
confidence
FP rate = product of black star rates
TP rate = red star rate – FP rate
Prediction
Self-Consistency
metric
 Unsupervised precision/recall

## Slide 38: Coincident Anomaly Detection (CoAD)
Consider two algorithms making predictions on two streams of data
We estimate unlabeled version of recall/precision from coincidence
Estimates can be differentiable  can train neural networks!
i.e. a loss function, not just a metric
Formally the loss function is defined for NN outputs :
: Estimated anomaly rate
: Weighting factor (recall vs. precision)
: red star rate
: estimated FP rate

## Slide 39: CoAD for RF Station Faults
RF Station data
Beam Data
Estimated precision/recall
Implementation for RF station task:
Network 1
Network 2
Unsupervised loss function
Anomaly confidence
Anomaly confidence

## Slide 40: Case Study 1: Performance in the control room
 | Precision | Recall (events)
Manual recording by operator | NA | 6
Status bit | 0.31 | 385
Coincident Detection | 0.88 | 504
6x fewer false positives vs. status bit
100x more anomalies vs. manual recording
30% more anomalies vs. status bit
Summary of predictions on 4 months of data
Ryan Humble, Finn O’Shea, Zhe Zhang
Live deployment in LCLS control room!
BPMs
RF
Amplitude

## Slide 41: Inverse problems: X-ray Pulse Reconstruction
Problem: absolute phase is meaningless!
SimulatedInput
power
Spectrum
Labeled loss,
Predicted Output
Simulated Output
field
field
NN Inverse Model
Approach #2: Train a labeled neural network
D. Ratner et al., Opt. Exp., 2021

## Slide 42: Inverse problems: X-ray Pulse Reconstruction
Input
power
Spectrum
power
Spectrum
Predicted Input
Predicted Output
Physics forward model, F
field
“Physics-informed neural network” (PINN)
Advantages: No need for labeled data, train directly on experimental data
NN Inverse Model
F
D. Ratner et al., Opt. Exp., 2021
Approach #3: Train a neural network with cycle-consistent loss
Unlabeled loss,